## Slide 1
Methodology Overview
Data & Model
Data Sources:
• LiDAR: 5m → PAD (3D fuel structure)
• Terrain: 5m DTM
• Fire: EMSR 685 delineations
3D CA Model:
• 20m resolution, 20 layers (0-40m)
• 3 spread mechanisms:
Horizontal, Vertical, Ember
Objective Function
Minimize: (1 - Dice) + P
Dice = 2|A∩B| / (|A|+|B|)
P = 2(r-2)² if r>2, else P=0
Rationale:
• Balances spatial accuracy
• Prevents unrealistic spread
• Standard in wildfire validation
Calibration Framework
Two-Stage Approach:
Stage 1: Sensitivity Analysis
• 16 parameters tested
• Range-based screening
• Top 4 parameters selected
Stage 2: Grid Search
• 3 points × 4 params = 81 runs
• Modified Dice optimization
Training: Days 1-2 (Aug 18-21)
Validation
Out-of-Sample Testing:
Test Period:
Days 3-4 (Aug 24-26)
Performance Metrics:
• Day 3: Dice = 0.690
• Day 4: Dice = 0.486
• Improvement: +29.6%
Ensures model generalization to unseen fire events